## Slide 1
Mechanical Measurements
Lesson 12

## Slide 2
hydraulic or pneumatic load cells: are employed to measure very big forces. The measurement is done “indirectly” passing through the pressure measurement of a particular fluid (generally oil)
the area “A” of the surface which compresses the fluid is a design parameter of the instrument The force F can then be calculated immediately from the pressure measurement !

## Slide 3
Measurement of PRESSURE : it is also an indirect measurement…
There are many measurement units for pressure :
pascal (Pa): in the International System = 1 newton over squared meter (1 N/m²) or kg·m−1·s−2
Baria: in the old CGS System (dina/cm²)
Bar: (105 Pa = 1 daN/cm²) submultiples of the bar are also widespread, in particular the millibar is used much in meteorology and the microbar in acustics
torr: the pressure exerted by a mercury column high 1 mm (133,3 Pa)
mm H2O: the pressure exerted by a water column high 1 mm (9,81 Pa)
atmosphere (atm): about equal to the pressure exerted by the atmosphere at sea level (101325 Pa = 760 mmHg = 760 torr)
Force kilogram (kgf): over cm² or over m²
Tecnical atmosphere (symbol: at or ata): equal to 1 kgf/cm2 (10.000mmH2O), little bit smaller than the physical atmosphere (0,96784 atm). Also known as ata, when understood as absolute pressure, and ate, when thought as relative pressure.

## Slide 4
Pressure P is technically measured by 3 different manometer types:
Liquid manometers
Metallic manometers
Electric manometers
Absolute pressure or real pressure (ata, absolute atm): is the pressure measured assuming the vacuum as reference pressure
Relative pressure (ate, relative atm): is the pressure measured assuming another pressure as reference pressure (typically the atmospheric pressure)

## Slide 5
Liquid manometers:
Differential (Prandtl) manometer or null-out manometer:
Based on a fluid which rises inside a tube due to the pressure:
A1>>A2
Absolute pressure

## Slide 6
Metallic manometers:
They are all based on the deformation of an elastic element caused by the pressure forces :

## Slide 7
Bourdon manometer …
What happens in section AA ?

## Slide 8
Plastic deformation? Systematic error

## Slide 9
Diaphragm membrane manometer:
Pressure-diaphragm rosette

## Slide 10
Electric manometers:
Capacitive transducers must be supplied with alternating current …
Notes: Piezoelettrico: applicazione stimolo meccanico – polarizzazione elettrica (e viceversa)

## Slide 11
Semiconductor silicon chip pressure transducer:
Square silicon chip:
- 4 piezoresistors
Wheatstone Bridge:
- 4 resistor changes
Pressure measurement:
- atmospheric pressure as reference
- differential pressure
- absolute (to vacuum)

## Slide 12
Diffused semiconductor pressure transducers use semiconductor material for the strain gauge elements. They are diffused into a silicon pressure sensing diaphragm

## Slide 13
Pressure gauge calibration bench:

## Slide 14
Piezo-resistive film pressure transducers :

## Slide 15
Sensing Area |  |  |  | Total |  | 
Width |  | Height |  | Sensels | Sensel Density | 
4.40 | in. | 4.40 | in. | 1,936 | 100.0 | in.2
111.8 | mm | 111.8 | mm | 1,936 | 15.5 | cm2
Thickness --> 0,2 mm

## Slide 17
Pressure mapping
In-shoes pressure mapping
Seating pressure analysis