## Slide 1
Numerical & Digital instruments
Numerical (and digital) instruments display the measurement information directly with numbers in digit format !
No mechanical indicator;
No indication delay;
No reading errors; …
The first numerical indicators were Light Emitting Diodes (LED): a semiconductor light source that emits light when current flows through it.
Made of gallium arsenide (GaS) and gallium phosphide (GaP) PN junctions directly polarized !
They use current and, therefore, they heat up … they were highly miniaturized … each diode is one of the seven light emitting bar !
Notes: Arseniuro di gallio
Fosfuro di gallio

## Slide 2
Liquid Cristal Display (LCD) are based on nematic crystal: much more efficient, because they DO NOT consume current …
The liquid crystal is placed between two polarising filters that are at 90° each other: together they form the part of the system that prevents light from passing through it or not.
When there is no electric voltage applied to the crystal, it twists light by 90°, which allows the light to pass through the second polariser and be reflected back.
When a voltage is applied, the crystal molecules align themselves, and the light cannot pass through the polariser: the segment turns black. Selective application of voltage to electrode segments creates the digits.
A simple black or white LCD display works by either allowing daylight to be reflected back out at the viewer or preventing it from doing so, in which case the viewer sees a black area.
7 electrode segments
dark segments
light
polarising filter
glass screen
electrode
liquid crystal molecules arragned in a spiral
aligned liquid crystal molecules
electrode
glass screen
polarising filter
reflected light
mirror

## Slide 3
Need of backlight
Each segment might be a single pixel
Advances in technology (miniaturization/low current)  LED

## Slide 4
Electronic and Digital Counters:
example of a number N = 8725,4 expressed in decadic base
example of a number N = 19 expressed in binary base
in summary form: 1 0 0 1 1
example of a number N = 147 expressed in binary base
in summary form: 1 0 0 1 0 0 1 1
Generic way of exploding the representation of a number !
It is easily seen, that in binary format the “coefficients” that are needed (the binary digits : bit) increase rapidly !
(shorter in the decadic base but with 10 tension levels)
A bit is an elementary information carrier !
However, in the electronic measurement instrumentation a special code system is employed: the BCD code (Binary Coded Decimal) which encodes in binary the individual decimal digits !
This is a pure binary code that encodes the ten digits from 0 to 9 with a four bit configuration …
Remember : with “n bits” we can count in binary up to 2n – 1

## Slide 5
The fundamental basic element for the electronic counting is the astable electronic multivibrator (FLIP – FLOP)
The FF changes status when it receives a trigger at its input, and “keeps the new status” until a new trigger is received at the input of the device:
Note on the left table:
4 bits = we count up to 24 – 1
Decimal Digit | Four-Bit Binary Equivalent | Binary-coded Decimal equivalent
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0010
3 | 0011 | 0011
4 | 0100 | 0100
5 | 0101 | 0101
6 | 0110 | 0110
7 | 0111 | 0111
8 | 1000 | 1000
9 | 1001 | 1001
10 | 1010 | Illegal
11 | 1011 | Illegal
12 | 1100 | Illegal
13 | 1101 | Illegal
14 | 1110 | Illegal
15 | 1111 | Illegal

## Slide 6
The "elementary circuit" is composed of a Flip – Flop (FF) together with a CR circuit and a rectifier diode
For every two triggers at the circuit input, we have only one trigger at the output !
The circuit divides by two the electric triggers received at its input !
If we connect four of these elementary cells in series, we have designed the electronic circuit that counts in the BCD code a single digit (from 0 to 9) :
Indicators L tell if the FF is in the High (X) or Low (O) status
n is the number of triggers received at the input !
Binary Coded Decimal (BCD) counter / Decade counter
X
X
X
X
A
B
C
D
E
n
L1
L3
L2
L4

## Slide 7
To get one trigger at the output we need 16 input triggers.. after that, the counter resets to zero again.
We recognize that the 4 Flip Flop (I1 I2 I4 I8) are the elementary (digital) memory cells which change the “combination of their status” depending on how many triggers are inputted to the device.
The four cells count in binary code:
LSB MSB
LSB = Least Significant Bit
MSB = Most Significant Bit
examples: 6 = 0 1 1 0
11 = 1 1 0 1
14 = 0 1 1 1
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
l1 l2 l4 l8
20 21 22 23
0
1

## Slide 8
However, to realize the BCD counter, we need the counter to count only up to 9: the remaining numbers (10 to 15) must be assigned illegal value … and to realize a decimal counter, we need also one trigger to be outputted every ten input triggers !
To obtain this result, we have to modify the electronic circuit, speeding up the trigger output by “sending some extra triggers” at the input with a double feedback:
After the “double feedback” we have at the input A: n+x+y triggers and at the feedback point C we have no more n/4 triggers, but
Because it is also y = x/2 and z = y/2
we can write: and n + 3y = 8y n = 5y or y= n/5 : and we reached our result !
X
X
X
X
A
B
C
D
E
n

## Slide 9
BCD counters with feedback can be “connected in series” so to count decimal numbers but, to be consistent with the way we read numbers the circuits must be rotated 180° and the triggers must be inputted from the right side !

## Slide 10
Time and Frequency Measurement:
If we connect to the BCD counter
an electronic gate,
a quartz clock,
an event input amplifier with a gate control
we can measure with high resolution the time between two events:
The clock is an electronic oscillator with a “fairly high” frequency (100 MHz) and is always on.
The gate control opens and closes the gate depending on the input signal level.
The triggers produced by the clock pass through the gate and are counted (n) by the BCD counter only during the period of time (t) for which the gate is open:
Electronic chronometer
1
7
1
5
Trigger level
Signal
Counted puses