## Slide 1
Mechanical Measurements
Lesson 9

## Slide 2
Length and displacement measurement
Many instruments are available to measure length and displacement in modern technology …
The most ancient is the graduated ruler:
It subdivides 19 mm in 20 parts (9 mm in 10 parts): each part is therefore 0,95 (0,9) mm long. When measuring, you count the first mobile notch coinciding with any fixed notch and you add that “0.05 (0.1) of millimeter” to your reading !
Rulers have an approximation of 1 mm,
7.35
Vernier Calipers have an approximation of 0,05 mm (1/20 caliper) or 0.1 (1/10 caliper), over an average range of 200 mm !

## Slide 3
If you need more resolution, you can use the Micrometer (Palmer): it is based on a “micrometric screw” with a pitch of 0.5 mm (sleeve). It has an approximation of 0,01 mm (over a range of 25 mm) !
There are 50 notches on the rotating screw (thimble), therefore for every notch the screw advances:
mm,
which is also the approximation of the instrument !
Of course the range is limited by the instrument screw opening …

## Slide 4
However in the industry, almost all the displacement transducers are electrical:
ELECTRICAL
TRANSDUCER
L
v , i
They are generally based on the Ohm’s law:
With the impedance:

## Slide 5
We have already seen the potentiometers, where and the graduation curve is:
with a constant sensitivity expressed in [V/m]
For rotational potentiometers we have:

## Slide 6
Capacitive transducers are all based on the fundamental physical relationship:
We can vary the “distance d” but then we do not get a constant sensitivity:
or we can vary the “plates surface S” (good for rotating capacitor transducers) and we get a constant sensitivity:
or we can even vary the “dielectric constant εr” and we get a constant sensitivity as well:

## Slide 7
Inductive transducers are a bit more complex, for example in the variable reluctance transducer the inductance
is changing because of a variation of
the magnetic circuit reluctance: where
and it is:
Because while even if
it basically results :
with a constant sensitivity :
X=la/2
Contactless / the circuit can be closed directly on the tool: width measurements
If we supply the coil with a “c.a. voltage” :
we can apply V = Z × I where
and the graduation curve is:

## Slide 8
There are also simpler inductive transducers which do not need a voltage supply, because they are based on
permanent magnets and on the Faraday’s law :
However, the output signal is proportional to the velocity of the displacement and needs to be integrated …
These are all contactless sensors !
Type (b) transducers are reversible and can become (with an appropriate design - changing the size of the elements) loudspeakers !
The graduation curve is:
A typical application of this kind of transducers is the microphone pick-up …  membrane
Acustic waves  e0

## Slide 9
courtesy of
“machinedesign.com”
Non contact detection of metallic objects
Very accurate
Only metallic
Limited range
Non contact detection of metallic and non metallic
Low cost
Less accurate, slower
Difficult in designing
Versitile  industrial sensing
More expensive
Not affected by environmental conditions
- Difficulties in reading reflections for soft, curved or small objects

## Slide 10
courtesy of
“machinedesign.com”

## Slide 11
The most important inductive transducer is the Linear Variable Dispalcement Transducer (LVDT)
One primary and two secondary coils are wrapped as in figure (a). A high permeability (μr>10000) inner nucleus (b) picks up the displacement and engages the magnetic field produced by the primary coil …
Input voltage Ei at the primary coil is, of course, a.c.
Because the secondary coils are winded series-opposing the resulting output voltage E0 will be differential:
with the mutual inductance coefficients
and with i = 1 , 2
Note that the relationship above is valid for “every time instant” and is also preliminary form of the LVDT graduation curve !
L1
L2

## Slide 12
The right figure explains what is happening when the ferromagnetic nucleus moves from the central null position, copying the external displacement. It can be easily seen that the LVDT is an electric “zero method” transducer !

## Slide 13
LVDT are not linear transducers but they can be considered liner in a limited range, near the central null position !
To read the output voltage, LVDT need a signal manipulation circuit that provides for the rectification of the signal E0 and a phase discriminator to understand if the displacement is happening towards the left or the right side !

## Slide 14
Example of rectifier and phase demodulator …
Dynamic example:
LVDT with a 10g nucleus, measuring a displacement of ± 1mm at 1 kHz
Displacement:
Acceleration (of the nucleus):
Whatever is the displacement we are measuring, to correctly pick up the ± 1mm amplitude at 1kHz frequency, the external displacement must apply to the nucleus a force:
which is maximum at the inversion points:
with and
the dynamic loading effect …

## Slide 15
Digital ENCODERS
Encoders are “native digital” motion transducers
They are simply made by coupling a notch trace and a notch reader in relative motion by each other. The distance δx (pitch) between two consecutive notches is the fundamental design data of the encoder.
In tachometric encoders we just read the number of notches the sensor counted to get the distance: x = n × δx.
The number of notches counted in each time unit gives us also the velocity of the motion !
Spatial resolution is equal to δx/2 but NO information about motion verse is provided by such transducer !

## Slide 16
Digital ENCODERS
Incremental encoders can overcome this limit by using two notch traces, staggered each other with a pitch of δx/4.
This is also the new enhanced resolution of the transducer.
0-1 transition: motion verse
NO information about the absolute position is provided by such transducer !

## Slide 17
Absolute encoders make a direct association between the actual position and a binary code !
They have as many notch traces (and readers) as the bit number that is needed !

## Slide 18
The natural binary code is not ideal for encoders because there are several transitions for which more that one bit is changing its state simultaneously ! This is not guaranteed in real devices and it can cause noise …
Therefore, encoders employ the grey binary code where, for every step, there is always only one bit at a time that changes its state !